## Slide 1
Applied Physics
Clipper Circuits
Mahek kalani & Teesha preetmani
Computer Science Department

## Slide 2
“Clipper circuit”
Also knows as Clipping circuit , limiters ,slicers e.t.c
AN application of diode
Definition:
An electronic circuit that clip off or removes a portion of an A.c signal ,without causing any distortion to the remaining part of wave form is called the clipper circuit .
OR
A clipper is a device that removes the either positive half (top) or negative half (bottom ) or some part
of positive or negative halves of A.c signal

## Slide 3
Note : A clipper does not distort the remaining part of waveform

## Slide 4
Why Clipper circuit ?
Electronic device or very sensitive to voltage . If a large amplitude of voltage is applied ,it may permanently destroy the device .so it is essential to protect the electronic circuit .
The protection of electronic device can be acheived by the using the clipper circuit (by reducing the voltage )

## Slide 5
“Example of clipper circuit”
Half wave rectifier

## Slide 6
Types of clipper circuit
Shunt negative clipper
Series positive clipper
Shunt positive clipper
Series negative clipper
Shunt diode clipper
Series diode clipper
Positive cycle
Negative cycle
Series positive clipper with Bias
Positive cycle
Negative cycle
Series positive clipper with Bias
Positive cycle
Negative cycle
Series positive clipper with Bias
Positive cycle
Negative cycle
Series positive clipper with Bias

## Slide 7
In series clipper circuits, the diode is connected in series with the output. In such clippers, the input signal appears at the output when the diode is forward biased and conducting.
It is divided into positive and negative clippers.
Series Positive Clippers
Series positive clippers remove or clips the positive half of the waveform. In a series positive clipper, the diode is in reverse biased and in series with the output as shown in the figure below.
Series Negative Clippers
During positive half cycle, the diode is forward biased due to the input voltage. Therefore, the input signal passes through the diode and appears at the output.
“Series Diode Clipper “

## Slide 8
During the negative half-cycle, the voltage at point A is negative than point B. The diode becomes forward bias and the signal pass through it. The signal appears across the Rl. Therefore, the negative half cycle passes through the circuit and appears at the output.
During the negative half cycle, the diode becomes reverse-biased and it does not conduct. Therefore, there is no voltage at the output and the negative half cycle is clipped from the input waveform
Series Positive Clippers with Bias
Positive Bias
In such a positive clipper circuit, the positive of the battery is connected to the P side of the diode as shown in the figure below.
Series Negative Clippers with bias
During the positive half cycle, the diode is forward biased due to input signal voltage. While it is reversed biased due to the battery voltage. the state of the diode depends on both the voltage sources. Therefore, the diode will be forward biased and conduct only if the input voltage is greater than the battery voltage.
Positive Bias

## Slide 9
During the negative half cycle, the diode is forward biased due to the input voltage as well as the battery voltage. Therefore, the input signal passes through the diode and it appears at the output
Negative Bias
During the positive half cycle, the diode is reversed biased due to the input voltage and the negative battery as well. Therefore, in the positive half cycle, the diode does not conduct and only the negative battery voltage appears at the output.
During the negative half of the cycle, the diode is reversed biased due to both the input voltage as well as the battery voltage. therefore, only battery voltage appears at the output for the whole negative half cycle.
Negative Bias
During the positive half cycle, the diode is forward biased due to both the input signal and the battery voltage. Therefore, the diode conducts the signal for the whole positive half cycle and it appears at the output as it is in the input.

## Slide 10
During the negative half-cycle, the input voltage polarity reverses and the diode becomes forward biased. However, the diode is reverse biased due to the negative battery. Therefore, the diode only becomes forward biased if the input voltage increases above the battery voltage and the input signal appear at the output. Otherwise, the negative battery voltage appears at the output.
During the negative half-cycle, the input voltage forces the diode in reverse bias but the battery voltage still forward biases the diode. During this whole cycle, the diode only conducts when the battery voltage exceeds the input voltage.

## Slide 11
“Applications of Clipper”
The main purpose of the clipper circuit is to modify the waveform of the signal which can be used in several applications such as in protection against overvoltage, noise removal, transmission, etc.
The clipper circuit offer overvoltage protection therefore, it is used in power supplies for limiting the voltage.
They are used for filtering noise in transmitters.
They are used in transmitters and receivers of television.
They are used for modifying or generating new waveforms such as square, triangular, etc.

## Slide 12
THANKYOU